## Slide 1: Rethinking the Union of Computed Tomography Reconstruction and GPGPU Computing for Industrial Applications
Edward S. Jimenez
San Diego State University, Computational Science Research Center Colloquium Series
March 15th, 2013

## Slide 2: Computed Tomography
Computed Tomography (CT) is an indirect 3D imaging technique.
Input: Set of X-ray images acquired about a center of rotation.
Output: Three-dimensional approximation of internal and external structure
Reconstruction: Convolution- Backprojection Algorithm (Feldkamp-Davis-Kress)
Geometry and Configuration of CT System determines magnification
Reconstruction algorithm is O(n4)
Image Source: http://www.xviewct.com/assets/images/how-ct-works.gif

## Slide 3: GPU
Graphics Processing Units are coprocessors that handle image manipulation and now are being used for general purpose computing.
Capable of Teraflops!
This massive computational capability of GPUs can be harnessed for many applications.
  Parallel computing environment
  Fast dedicated memory
  Fast Cache
CT Reconstruction from projection images requires many arithmetic and trigonometric operations for every volumetric pixel (voxel).

## Slide 4: CT on GPUs
“Porting” CT reconstruction on GPUs has shown major bottlenecks.
  Usually not an issue with medical datasets.
  Memory uploads/downloads to device (GPU).
  What ratio of x-ray data to volume should be allocated?
Traditional CPU-based code reconstructed one slice at a time
  Predicable memory access even when multi-threaded.
GPU-based reconstruction
  Massively multithreaded environment creates scattered memory reads if large x-ray data is utilized per kernel launch.
  Scattered Memory reads present for large volume storage too!
  Suddenly reconstruction becomes an Irregular Problem!

## Slide 5: Approach
Maximize resources by blocking x-ray data and sub-volumes.
Counter Intuitive: Maximize x-ray data uploads to device!
  Partition x-ray images and batch small x-ray image subsets
Volume: Use most GPU memory for direct volume storage.
Utilize GPU-Specific Hardware/Features
  Massive parallelism
  Texture memory/Texture Cache
  Constant Memory
  Data prefetch to pinned memory for fast upload
Dynamic Task Partitioning

## Slide 6: Implementation
CUDA Programming environment and C++
Minimum requirements
  Fermi-based Architecture
  1 GB Device memory
  At least one x-ray sub image and one slice must fit simultaneously
Allows for 1 – 8 GPUs per node
Dynamic Partitioning determined by slice-to-texture ratio (STR)
STR may not always be satisfied:
  Resource maximization vs. Awkward task size
  Reconstruction size – Too large or small?
  Tail-end reconstruction

## Slide 7: Dynamic GPU Tasking
For a given subvolume the amount of x-ray data necessary varies
  Due to the geometry of the system.
  Taken into account with STR to determine memory data allocation on device.
  Typically, reconstruction along center slices require less data.
Using OpenMP 2.0, a CPU thread controls one GPU in the system
  Each GPU will usually be reconstructing sub-volumes of varying size
  Load balancing difficult if subvolume is fixed for all GPUs
No synchronization necessary for CPU threads while algorithm is executing.
No synchronization necessary between GPU threads either.
One atomic operation to update reconstruction progress and determine next subvolume to reconstruct.

## Slide 8: FDK Kernel Layout
Input: X-ray data, index, and size, subvolume data, index, and size, system geometry
Get thread ID and voxel positions p1, . . . , ps based on ID
  if Thread ID position within ROI then
    for Every slice j in slice block do
      Set register value to zero
      for Every image i in image subset do
        Determine texture interpolation coordinate in image i
        Update register value with texture fetch and scaling
      end for
      Update voxel pj in global memory with register value
    End for
  End if

## Slide 9: GPU Cache Hierarchy
L2 Cache
L1 Cache
Texture Cache
Constant memory
Device Memory
Register

## Slide 10: Evaluation
Supermicro workstation
  Dual Hexacore Intel Xeon X5690 @ 3.46 GHz w/ hyper threading
  192 GB RAM
  4 PCI-E 2.0 x16 slots
2 NVidia S2090 Devices
  4 Tesla M2090 GPUs each (8 total)
  Connected via 4 PCI-E host interface cards
M2090
  6 GB GDDR5 memory apiece
  16 streaming multiprocessors (SM)
  768 KB L2 Cache (load, store, and texture operations)
  32 Compute cores per SM
  48 KB L1 Memory (explicitly set, shared memory not used)
  8 KB Constant Memory and Texture Cache
Two datasets tested
  64 Gigavoxels
  1 Teravoxel

## Slide 11: Results: Throughput 64 GV/ 1 GPU

## Slide 12: Results: Throughput 64 GV/ 8 GPUs

## Slide 13: Results: Throughput 1 TV/ 1 GPU

## Slide 14: Results: Throughput 1 TV/ 8 GPUs

## Slide 15: Results: L1 Cache Hit-rates

## Slide 16: Results: L2 and Texture Cache Hit-rates

## Slide 17: Milestones
Original Proposal
  Create a HPC Multi GPU-based approach to reconstruction
    Created Flexible Implementation
      Laptop, Desktop, High-End Workstation, Cluster
    All implementations have been tested with up to 8 GPUs
      Did not find any papers that utilized 8 GPUs
  Data movement to be optimized with Multi-Resolution Parallelization
    CUDA (8096 Active Parallel Threads)
    OpenMP (~24-32 Parallel Threads)
    MPI (Almost Arbitrary number of nodes)

## Slide 18: Milestones Continued
Original Proposal:
  Concurrent Data movement and computation
    Data Queuing (Concurrent Data/Computations)
    Dynamic Task Allocation (Maximize GPU Resources)
    Pinned Memory (Improve Memory Transfers to GPU)
  Will be 20 times faster than traditional CPU approaches
    Single Thread: 260-3313 times faster
    Multi-Thread: 33-328 times faster
    GPU-Port: ~10-40 times faster
    Impact: Hours-to-minutes/Year-to-hours
  Overall Impact
    Used by multiple organizations at SNL
    LANL wants a copy!

## Slide 19: Performance Evaluation
Large-Scale CT Reconstruction algorithms clearly benefit from an Irregular approach
  Massive parallelism has potential to destroy spatial locality
  Counter Intuitive approach may create performance gains
  Irregular approach improves voxel throughput by improving cache-hit rates
  Small X-ray data batches and large subvolume tend to perform best.
Are there other CPU-based algorithms that become irregular if implemented efficiently on a GPU?
I/O is killing performance times!

## Slide 20: Modularized Approach
Can we modularize the algorithm?
Leverage the multi-threaded nature of modern CPUs
MIMD implementation
  Memory Allocation/Data Input Reads
  GPU Control/ Data Writing
The goal is to keep the GPUs from idling
  When slices are reconstructed, transfer to system memory and fetch next block to reconstruct
  Separate thread responsible for writing data to disk

## Slide 21: MIMD
  Memory Allocation/Data Input Reads
  One thread: Allocate temporary memory storage
  Other threads: Read in X-ray image data in parallel
GPU Control/Data Writing
  N threads: Each thread controls one of N GPUs
    Maximize GPU resources, queue data blocks, data transfer
  Complement Threads: Wait for slices to write to disk
    Data formatting, compression, writing
GPU performance less dependent on disk storage performance

## Slide 22: Results
64 Billion Voxels
  Original: 30 minutes
  Modularized: 18 minutes
1 Trillion Voxels
  Original: 22 Hours
  Modularized: 19 Hours, 22 minutes

## Slide 23: Future Work
Power requirement studies
Iterative reconstruction
Real-time CT
Non-traditional processing approaches